## C Protocol 1.0
### C Read Write Protocol 1.0
- Description
  This example writes Goal Position to Dynamixel and reads Present Position of Dynamixel until it stops moving. The functions that are related with the Read and the Write handle the number of items which are near each other in the Dynamixel control table, such as the goal position and the goal velocity.
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
  /*
  * read_write.c
  *
  * Created on: 2016. 5. 16.
  * Author: Leon Ryu Woon Jung
  */

  //
  // ********* Read and Write Example *********
  //
  //
  // Available DXL model on this example : All models using Protocol 1.0
  // This example is designed for using a Dynamixel MX-28, and an USB2DYNAMIXEL.
  // To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
  // Be sure that Dynamixel MX properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000 [1M])
  //

  #ifdef __linux__
  #include <unistd.h>
  #include <fcntl.h>
  #include <termios.h>
  #elif defined(_WIN32) || defined(_WIN64)
  #include <conio.h>
  #endif

  #include <stdlib.h>
  #include <stdio.h>
  #include "dynamixel_sdk.h" // Uses Dynamixel SDK library

  // Control table address
  #define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
  #define ADDR_MX_GOAL_POSITION 30
  #define ADDR_MX_PRESENT_POSITION 36

  // Protocol version
  #define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

  // Default setting

  #define DXL_ID 1 // Dynamixel ID: 1
  #define BAUDRATE 1000000
  #define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

  #define TORQUE_ENABLE 1 // Value for enabling the torque
  #define TORQUE_DISABLE 0 // Value for disabling the torque
  #define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
  #define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
  #define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

  #define ESC_ASCII_VALUE 0x1b

  int getch()
  {
  #ifdef __linux__
    struct termios oldt, newt;
    int ch;
    tcgetattr(STDIN_FILENO, &oldt);
    newt = oldt;
    newt.c_lflag &= ~(ICANON | ECHO);
    tcsetattr(STDIN_FILENO, TCSANOW, &newt);
    ch = getchar();
    tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
    return ch;
  #elif defined(_WIN32) || defined(_WIN64)
    return _getch();
  #endif
  }

  int kbhit(void)
  {
  #ifdef __linux__
    struct termios oldt, newt;
    int ch;
    int oldf;

    tcgetattr(STDIN_FILENO, &oldt);
    newt = oldt;
    newt.c_lflag &= ~(ICANON | ECHO);
    tcsetattr(STDIN_FILENO, TCSANOW, &newt);
    oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
    fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

    ch = getchar();

    tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
    fcntl(STDIN_FILENO, F_SETFL, oldf);

    if (ch != EOF)
    {
      ungetc(ch, stdin);
      return 1;
    }

    return 0;
  #elif defined(_WIN32) || defined(_WIN64)
    return _kbhit();
  #endif
  }

  int main()
  {
    // Initialize PortHandler Structs
    // Set the port path
    // Get methods and members of PortHandlerLinux or PortHandlerWindows
    int port_num = portHandler(DEVICENAME);

    // Initialize PacketHandler Structs
    packetHandler();

    int index = 0;
    int dxl_comm_result = COMM_TX_FAIL; // Communication result
    int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

    uint8_t dxl_error = 0; // Dynamixel error
    uint16_t dxl_present_position = 0; // Present position

    // Open port
    if (openPort(port_num))
    {
      printf("Succeeded to open the port!\n");
    }
    else
    {
      printf("Failed to open the port!\n");
      printf("Press any key to terminate...\n");
      getch();
      return 0;
    }

    // Set port baudrate
    if (setBaudRate(port_num, BAUDRATE))
    {
      printf("Succeeded to change the baudrate!\n");
    }
    else
    {
      printf("Failed to change the baudrate!\n");
      printf("Press any key to terminate...\n");
      getch();
      return 0;
    }

    // Enable DXL Torque
    write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }
    else
    {
      printf("Dynamixel has been successfully connected \n");
    }

    while (1)
    {
      printf("Press any key to continue! (or press ESC to quit!)\n");
      if (getch() == ESC_ASCII_VALUE)
        break;

      // Write goal position
      write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
      if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      do
      {
        // Read present position
        dxl_present_position = read2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_PRESENT_POSITION);
        if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
        {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
        }
        else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
        {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
        }

        printf("[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL_ID, dxl_goal_position[index], dxl_present_position);

      } while ((abs(dxl_goal_position[index] - dxl_present_position) > DXL_MOVING_STATUS_THRESHOLD));

      // Change goal position
      if (index == 0)
      {
        index = 1;
      }
      else
      {
        index = 0;
      }
    }

    // Disable Dynamixel Torque
    write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Close port
    closePort(port_num);

    return 0;
  }
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdlib.h>
The function abs() is in the example code, and it needs stdlib.h to be included.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36
Dynamixel series have their own control tables: Addresses and Byte Length in each items. To control one of the items, its address (and length if necessary) is required. Find your requirements in http://emanual.robotis.com/.

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL_ID 1 // Dynamixel ID: 1
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b
Here we set some variables to let you freely change them and use them to run the example code.
As the document already said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.
Dynamixel basically needs the TORQUE_ENABLE to be rotating or give you its internal information. On the other hand, it doesn’t need torque enabled if you get your goal, so finally do TORQUE_DISABLE to prepare to the next sequence.
Since the Dynamixel has its own rotation range, it may shows malfunction if your request on your dynamixel is out of range. For example, Dynamixel MX-28 and Dynamixel PRO 54-200 has its rotatable range as 0 ~ 4028 and -250950 ~ 250950, each.
DXL_MOVING_STATUS_THRESHOLD acts as a criteria for verifying its rotation stopped.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl_present_position = 0; // Present position

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable DXL Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel has been successfully connected \n");
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read present position
      dxl_present_position = read2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL_ID, dxl_goal_position[index], dxl_present_position);

    } while ((abs(dxl_goal_position[index] - dxl_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port
  closePort(port_num);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);
portHandler() function sets port path as DEVICENAME and get port_num, and prepares an appropriate functions for port control in controller OS automatically. port_num would be used in many functions in the body of the code to specify the port for use.

  // Initialize PacketHandler Structs
  packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = {DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE}; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl_present_position = 0; // Present position
index variable points the direction to where the Dynamixel should be rotated.
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_goal_position stores goal points of Dynamixel rotation.
dxl_error shows the internal error in Dynamixel.
dxl_present_position views where now it points out.

  // Open port
  if (openPort(port_num))
  {
      printf("Succeeded to open the port!\n");
  }
  else
  {
      printf("Failed to open the port!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
First, controller opens #port_num port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.
  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
      printf("Succeeded to change the baudrate!\n");
  }
  else
  {
      printf("Failed to change the baudrate!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Secondly, the controller sets the communication BAUDRATE at #port_num port opened previously.

  // Enable DXL Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel has been successfully connected \n");
  }
As mentioned in the document, above code enables Dynamixel torque to set its status as being ready to move.
write1ByteTxRx() function orders to the #DXL_ID Dynamixel in PROTOCOL_VERSION communication protocol through #port_num port, writing 1 byte of TORQUE_ENABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read present position
      dxl_present_position = read2ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL_ID, dxl_goal_position[index], dxl_present_position);

    } while ((abs(dxl_goal_position[index] - dxl_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }
During while() loop, the controller writes and reads the Dynamixel position through packet transmission/reception(Tx/Rx).
To continue its rotation, press any key except ESC.
write2ByteTxRx() function orders to the #DXL_ID Dynamixel in PROTOCOL_VERSION communication protocol through #port_num port, writing 2 byte of dxl_goal_position[index] value to ADDR_MX_GOAL_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
read2ByteTxRx() function orders to the #DXL_ID Dynamixel in PROTOCOL_VERSION communication protocol through #port_num port, requesting 2 bytes of value in ADDR_MX_PRESENT_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
Reading its present position will be ended when absolute value of (dxl_goal_position[index] - dxl_present_position) becomes smaller then DXL_MOVING_STATUS_THRESHOLD.
At last, it changes its direction to the counter-wise and waits for extra key input.

  // Disable Dynamixel Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
The controller frees the Dynamixel to be idle.
write1ByteTxRx() function orders to the #DXL_ID Dynamixel in PROTOCOL_VERSION communication protocol through #port_num port, writing 1 byte of TORQUE_DISABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
  // Close port
  closePort(port_num);

  return 0;
Finally, port becomes disposed.

### C Multi Port Protocol 1.0
- Description
  This example writes Goal Positions to two Dynamixels connected via two ports and reads their Present Positions until they stop moving.
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
/*
* multi_port.c
*
* Created on: 2016. 5. 16.
* Author: Leon Ryu Woon Jung
*/

//
// ********* Multi Port Example *********
//
//
// Available Dynamixel model on this example : All models using Protocol 1.0
// This example is designed for using two Dynamixel MX-28, and two USB2DYNAMIXEL.
// To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
// Be sure that Dynamixel MX properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000 [1M])
//

#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

#include <stdlib.h>
#include <stdio.h>
#include "dynamixel_sdk.h" // Uses Dynamixel SDK library

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME1 "/dev/ttyUSB0" // Check which port is being used on your controller
#define DEVICENAME2 "/dev/ttyUSB1" // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);

  // Initialize PacketHandler Structs
  packetHandler();

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position

  // Open port1
  if (openPort(port_num1))
  {
    printf("Succeeded to open the port1!\n");
  }
  else
  {
    printf("Failed to open the port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
    printf("Succeeded to open the port2!\n");
  }
  else
  {
    printf("Failed to open the port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
    printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
    printf("Failed to change the baudrate port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
    printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
    printf("Failed to change the baudrate port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read Dynamixel#1 present position
        dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      // Read Dynamixel#2 present position
      dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

    } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
}
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif
This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdlib.h>
The function abs() is in the example code, and it needs stdlib.h to be included.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36
Dynamixel series have their own control tables: Addresses and Byte Length in each items. To control one of the items, its address (and length if necessary) is required. Find your requirements in http://emanual.robotis.com/.

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME1 "/dev/ttyUSB0" // Check which port is being used on your controller
#define DEVICENAME2 "/dev/ttyUSB1" // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b
Here we set some variables to let you freely change them and use them to run the example code.
As the document previously said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.
The example uses two Dynamixels DXL1_ID, DXL2_ID connected with each ports DEVICENAME1, DEVICENAME2
Dynamixel basically needs the TORQUE_ENABLE to be rotating or give you its internal information. On the other hand, it doesn’t need torque enabled if you get your goal, so finally do TORQUE_DISABLE to prepare to the next sequence.
Since the Dynamixel has its own rotation range, it may shows malfunction if your request on your dynamixel is out of range. For example, Dynamixel MX-28 and Dynamixel PRO 54-200 has its rotatable range as 0 ~ 4028 and -250950 ~ 250950, each.
DXL_MOVING_STATUS_THRESHOLD acts as a criteria for verifying its rotation stopped.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);

  // Initialize PacketHandler Structs
  packetHandler();

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position

  // Open port1
  if (openPort(port_num1))
  {
    printf("Succeeded to open the port1!\n");
  }
  else
  {
    printf("Failed to open the port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
    printf("Succeeded to open the port2!\n");
  }
  else
  {
    printf("Failed to open the port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
    printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
    printf("Failed to change the baudrate port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
    printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
    printf("Failed to change the baudrate port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read Dynamixel#1 present position
        dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      // Read Dynamixel#2 present position
      dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

    } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);
portHandler() function sets port path as DEVICENAME1 and DEVICENAME2 and get port_num1 and port_num2 each, and prepares an appropriate functions for port control in controller OS automatically. port_num1 and port_num2 would be used in many functions in the body of the code to specify the port for use.

  // Initialize PacketHandler Structs
  packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = {DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE}; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position
index variable points the direction to where the Dynamixel should be rotated.
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_goal_position stores goal points of Dynamixel rotation.
dxl_error shows the internal error in Dynamixel.
dxl1_present_position and dxl2_present_position view where now each Dynamixel points out.

  // Open port1
  if (openPort(port_num1))
  {
      printf("Succeeded to open the port1!\n");
  }
  else
  {
      printf("Failed to open the port1!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
      printf("Succeeded to open the port2!\n");
  }
  else
  {
      printf("Failed to open the port2!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
First, controller opens #port_num1 and #port_num2 port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
      printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
      printf("Failed to change the baudrate port1!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
      printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
      printf("Failed to change the baudrate port2!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Secondly, the controller sets the communication BAUDRATE at #port_num1 and #port_num2 port opened previously.

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }
As mentioned in the document, above code enables each Dynamixel`s torque to set their status as being ready to move.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 1 byte of TORQUE_ENABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

while (1)
{
  printf("Press any key to continue! (or press ESC to quit!)\n");
  if (getch() == ESC_ASCII_VALUE)
    break;

  // Write Dynamixel#1 goal position
  write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Write Dynamixel#2 goal position
  write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  do
  {
    // Read Dynamixel#1 present position
    dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Read Dynamixel#2 present position
    dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

  } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

  // Change goal position
  if (index == 0)
  {
    index = 1;
  }
  else
  {
    index = 0;
  }
}
During while() loop, the controller writes and reads each Dynamixel position through packet transmission/reception(Tx/Rx).
To continue their rotation, press any key except ESC.
write2ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 2 byte of dxl_goal_position[index] value to ADDR_MX_GOAL_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
read2ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, requesting 2 bytes of value in ADDR_MX_PRESENT_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
Reading their present position will be ended when absolute value of (dxl1_goal_position[index] - dxl1_present_position) or (dxl2_goal_position[index] - dxl2_present_position) becomes smaller then DXL_MOVING_STATUS_THRESHOLD.
At last, it changes their direction to the counter-wise and waits for extra key input.

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
The controller frees the Dynamixels to be idle.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 1 byte of TORQUE_DISABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
Finally, ports become disposed.

Edit on GitHub
### C Multi Port Protocol 1.0
- Description
  This example writes Goal Positions to two Dynamixels connected via two ports and reads their Present Positions until they stop moving.
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
/*
* multi_port.c
*
* Created on: 2016. 5. 16.
* Author: Leon Ryu Woon Jung
*/

//
// ********* Multi Port Example *********
//
//
// Available Dynamixel model on this example : All models using Protocol 1.0
// This example is designed for using two Dynamixel MX-28, and two USB2DYNAMIXEL.
// To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
// Be sure that Dynamixel MX properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000 [1M])
//

#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

#include <stdlib.h>
#include <stdio.h>
#include "dynamixel_sdk.h" // Uses Dynamixel SDK library

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME1 "/dev/ttyUSB0" // Check which port is being used on your controller
#define DEVICENAME2 "/dev/ttyUSB1" // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);

  // Initialize PacketHandler Structs
  packetHandler();

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position

  // Open port1
  if (openPort(port_num1))
  {
    printf("Succeeded to open the port1!\n");
  }
  else
  {
    printf("Failed to open the port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
    printf("Succeeded to open the port2!\n");
  }
  else
  {
    printf("Failed to open the port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
    printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
    printf("Failed to change the baudrate port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
    printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
    printf("Failed to change the baudrate port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read Dynamixel#1 present position
        dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      // Read Dynamixel#2 present position
      dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

    } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
}
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif
This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdlib.h>
The function abs() is in the example code, and it needs stdlib.h to be included.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36
Dynamixel series have their own control tables: Addresses and Byte Length in each items. To control one of the items, its address (and length if necessary) is required. Find your requirements in http://emanual.robotis.com/.
// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME1 "/dev/ttyUSB0" // Check which port is being used on your controller
#define DEVICENAME2 "/dev/ttyUSB1" // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b
Here we set some variables to let you freely change them and use them to run the example code.
As the document previously said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.
The example uses two Dynamixels DXL1_ID, DXL2_ID connected with each ports DEVICENAME1, DEVICENAME2
Dynamixel basically needs the TORQUE_ENABLE to be rotating or give you its internal information. On the other hand, it doesn’t need torque enabled if you get your goal, so finally do TORQUE_DISABLE to prepare to the next sequence.
Since the Dynamixel has its own rotation range, it may shows malfunction if your request on your dynamixel is out of range. For example, Dynamixel MX-28 and Dynamixel PRO 54-200 has its rotatable range as 0 ~ 4028 and -250950 ~ 250950, each.
DXL_MOVING_STATUS_THRESHOLD acts as a criteria for verifying its rotation stopped.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);

  // Initialize PacketHandler Structs
  packetHandler();

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position

  // Open port1
  if (openPort(port_num1))
  {
    printf("Succeeded to open the port1!\n");
  }
  else
  {
    printf("Failed to open the port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
    printf("Succeeded to open the port2!\n");
  }
  else
  {
    printf("Failed to open the port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
    printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
    printf("Failed to change the baudrate port1!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
    printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
    printf("Failed to change the baudrate port2!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Read Dynamixel#1 present position
        dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      // Read Dynamixel#2 present position
      dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
      if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
      {
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
      }
      else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
      {
        printRxPacketError(PROTOCOL_VERSION, dxl_error);
      }

      printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

    } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num1 = portHandler(DEVICENAME1);
  int port_num2 = portHandler(DEVICENAME2);
portHandler() function sets port path as DEVICENAME1 and DEVICENAME2 and get port_num1 and port_num2 each, and prepares an appropriate functions for port control in controller OS automatically. port_num1 and port_num2 would be used in many functions in the body of the code to specify the port for use.

  // Initialize PacketHandler Structs
  packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  int dxl_goal_position[2] = {DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE}; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0, dxl2_present_position = 0; // Present position
index variable points the direction to where the Dynamixel should be rotated.
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_goal_position stores goal points of Dynamixel rotation.
dxl_error shows the internal error in Dynamixel.
dxl1_present_position and dxl2_present_position view where now each Dynamixel points out.

  // Open port1
  if (openPort(port_num1))
  {
      printf("Succeeded to open the port1!\n");
  }
  else
  {
      printf("Failed to open the port1!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }

  // Open port2
  if (openPort(port_num2))
  {
      printf("Succeeded to open the port2!\n");
  }
  else
  {
      printf("Failed to open the port2!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
First, controller opens #port_num1 and #port_num2 port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.

  // Set port1 baudrate
  if (setBaudRate(port_num1, BAUDRATE))
  {
      printf("Succeed to change the baudrate port1!\n");
  }
  else
  {
      printf("Failed to change the baudrate port1!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }

  // Set port2 baudrate
  if (setBaudRate(port_num2, BAUDRATE))
  {
      printf("Succeed to change the baudrate port2!\n");
  }
  else
  {
      printf("Failed to change the baudrate port2!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Secondly, the controller sets the communication BAUDRATE at #port_num1 and #port_num2 port opened previously.

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }
As mentioned in the document, above code enables each Dynamixel`s torque to set their status as being ready to move.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 1 byte of TORQUE_ENABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

while (1)
{
  printf("Press any key to continue! (or press ESC to quit!)\n");
  if (getch() == ESC_ASCII_VALUE)
    break;

  // Write Dynamixel#1 goal position
  write2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Write Dynamixel#2 goal position
  write2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  do
  {
    // Read Dynamixel#1 present position
    dxl1_present_position = read2ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_PRESENT_POSITION);
    if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Read Dynamixel#2 present position
    dxl2_present_position = read2ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_PRESENT_POSITION);
    if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    printf("[ID:%03d] GoalPos:%03d PresPos:%03d\t[ID:%03d] GoalPos:%03d PresPos:%03d\n", DXL1_ID, dxl_goal_position[index], dxl1_present_position, DXL2_ID, dxl_goal_position[index], dxl2_present_position);

  } while ((abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD) || (abs(dxl_goal_position[index] - dxl2_present_position) > DXL_MOVING_STATUS_THRESHOLD));

  // Change goal position
  if (index == 0)
  {
    index = 1;
  }
  else
  {
    index = 0;
  }
}
During while() loop, the controller writes and reads each Dynamixel position through packet transmission/reception(Tx/Rx).
To continue their rotation, press any key except ESC.
write2ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 2 byte of dxl_goal_position[index] value to ADDR_MX_GOAL_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
read2ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, requesting 2 bytes of value in ADDR_MX_PRESENT_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
Reading their present position will be ended when absolute value of (dxl1_goal_position[index] - dxl1_present_position) or (dxl2_goal_position[index] - dxl2_present_position) becomes smaller then DXL_MOVING_STATUS_THRESHOLD.
At last, it changes their direction to the counter-wise and waits for extra key input.

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num1, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num1, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num1, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num2, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num2, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num2, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
The controller frees the Dynamixels to be idle.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num1 and #port_num2 ports, writing 1 byte of TORQUE_DISABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

  // Close port1
  closePort(port_num1);

  // Close port2
  closePort(port_num2);

  return 0;
Finally, ports become disposed.
© 2019 ROBOTIS. Powered by Jekyll & Minimal Mistakes.

Edit on GitHub
### C Bulk Read Protocol 1.0
- Description
  This example writes Goal Positions to two Dynamixels simultaneously and repeats to read each present positions until Dynamixels stop moving. The funtions that are related with the Syncwrite handle the number of items that are near to each other in the Dynamixel control table on multiple Dynamixels, such as the goal position and the goal velocity.
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
/*
* bulk_read.c
*
* Created on: 2016. 5. 16.
* Author: Leon Ryu Woon Jung
*/

//
// ********* Bulk Read Example *********
//
//
// Available Dynamixel model on this example : MX or X series set to Protocol 1.0
// This example is designed for using two Dynamixel MX-28, and an USB2DYNAMIXEL.
// To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
// Be sure that Dynamixel MX properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000)
//
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

#include <stdlib.h>
#include <stdio.h>
#include "dynamixel_sdk.h" // Uses Dynamixel SDK library

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36
#define ADDR_MX_MOVING 46

// Data Byte Length
#define LEN_MX_GOAL_POSITION 2
#define LEN_MX_PRESENT_POSITION 2
#define LEN_MX_MOVING 1

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  // Initialize Groupbulkread Structs
  int group_num = groupBulkRead(port_num, PROTOCOL_VERSION);

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  uint8_t dxl_addparam_result = False; // AddParam result
  uint8_t dxl_getdata_result = False; // GetParam result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0; // Present position
  uint8_t dxl2_moving = 0; // Dynamixel moving status

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  // Add parameter storage for Dynamixel#1 present position value
  dxl_addparam_result = groupBulkReadAddParam(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
  if (dxl_addparam_result != True)
  {
    fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL1_ID);
    return 0;
  }

  // Add parameter storage for Dynamixel#2 present moving value
  dxl_addparam_result = groupBulkReadAddParam(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
  if (dxl_addparam_result != True)
  {
    fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL2_ID);
    return 0;
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Bulkread present position and moving status
      groupBulkReadTxRxPacket(group_num);
      if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);

      dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
      if (dxl_getdata_result != True)
      {
        fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL1_ID);
        return 0;
      }

      dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
      if (dxl_getdata_result != True)
      {
        fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL2_ID);
        return 0;
      }

      // Get Dynamixel#1 present position value
      dxl1_present_position = groupBulkReadGetData(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);

      // Get Dynamixel#2 moving status value
      dxl2_moving = groupBulkReadGetData(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);

      printf("[ID:%03d] Present Position : %d \t [ID:%03d] Is Moving : %d\n", DXL1_ID, dxl1_present_position, DXL2_ID, dxl2_moving);

    } while (abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD);

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port
  closePort(port_num);

  return 0;
}
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif
This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdlib.h>
The function abs() is in the example code, and it needs stdlib.h to be included.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Control table address
#define ADDR_MX_TORQUE_ENABLE 24 // Control table address is different in Dynamixel model
#define ADDR_MX_GOAL_POSITION 30
#define ADDR_MX_PRESENT_POSITION 36

// Data Byte Length
#define LEN_MX_GOAL_POSITION 2
#define LEN_MX_PRESENT_POSITION 2
Dynamixel series have their own control tables: Addresses and Byte Length in each items. To control one of the items, its address (and length if necessary) is required. Find your requirements in http://emanual.robotis.com/.

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL1_ID 1 // Dynamixel#1 ID: 1
#define DXL2_ID 2 // Dynamixel#2 ID: 2
#define BAUDRATE 1000000
#define DEVICENAME1 "/dev/ttyUSB0" // Check which port is being used on your controller

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque
#define DXL_MINIMUM_POSITION_VALUE 100 // Dynamixel will rotate between this value
#define DXL_MAXIMUM_POSITION_VALUE 4000 // and this value (note that the Dynamixel would not move when the position value is out of movable range. Check e-manual about the range of the Dynamixel you use.)
#define DXL_MOVING_STATUS_THRESHOLD 10 // Dynamixel moving status threshold

#define ESC_ASCII_VALUE 0x1b
Here we set some variables to let you freely change them and use them to run the example code.
As the document previously said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.
The example uses two Dynamixels DXL1_ID, DXL2_ID connected with the port DEVICENAME.
Dynamixel basically needs the TORQUE_ENABLE to be rotating or give you its internal information. On the other hand, it doesn’t need torque enabled if you get your goal, so finally do TORQUE_DISABLE to prepare to the next sequence.
Since the Dynamixel has its own rotation range, it may shows malfunction if your request on your dynamixel is out of range. For example, Dynamixel MX-28 and Dynamixel PRO 54-200 has its rotatable range as 0 ~ 4028 and -250950 ~ 250950, each.
DXL_MOVING_STATUS_THRESHOLD acts as a criteria for verifying its rotation stopped.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  // Initialize Groupbulkread Structs
  int group_num = groupBulkRead(port_num, PROTOCOL_VERSION);

  int index = 0;
  int dxl_comm_result = COMM_TX_FAIL; // Communication result
  uint8_t dxl_addparam_result = False; // AddParam result
  uint8_t dxl_getdata_result = False; // GetParam result
  int dxl_goal_position[2] = { DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE }; // Goal position

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl1_present_position = 0; // Present position
  uint8_t dxl2_moving = 0; // Dynamixel moving status

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Enable Dynamixel#1 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
  }

  // Enable Dynamixel#2 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
  }

  // Add parameter storage for Dynamixel#1 present position value
  dxl_addparam_result = groupBulkReadAddParam(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
  if (dxl_addparam_result != True)
  {
    fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL1_ID);
    return 0;
  }

  // Add parameter storage for Dynamixel#2 present moving value
  dxl_addparam_result = groupBulkReadAddParam(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
  if (dxl_addparam_result != True)
  {
    fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL2_ID);
    return 0;
  }

  while (1)
  {
    printf("Press any key to continue! (or press ESC to quit!)\n");
    if (getch() == ESC_ASCII_VALUE)
      break;

    // Write Dynamixel#1 goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    // Write Dynamixel#2 goal position
    write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
    {
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    }
    else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
    {
      printRxPacketError(PROTOCOL_VERSION, dxl_error);
    }

    do
    {
      // Bulkread present position and moving status
      groupBulkReadTxRxPacket(group_num);
      if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
        printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);

      dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
      if (dxl_getdata_result != True)
      {
        fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL1_ID);
        return 0;
      }

      dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
      if (dxl_getdata_result != True)
      {
        fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL2_ID);
        return 0;
      }

      // Get Dynamixel#1 present position value
      dxl1_present_position = groupBulkReadGetData(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);

      // Get Dynamixel#2 moving status value
      dxl2_moving = groupBulkReadGetData(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);

      printf("[ID:%03d] Present Position : %d \t [ID:%03d] Is Moving : %d\n", DXL1_ID, dxl1_present_position, DXL2_ID, dxl2_moving);

    } while (abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD);

    // Change goal position
    if (index == 0)
    {
      index = 1;
    }
    else
    {
      index = 0;
    }
  }

  // Disable Dynamixel#1 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Disable Dynamixel#2 Torque
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Close port
  closePort(port_num);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

// Initialize PortHandler Structs
// Set the port path
// Get methods and members of PortHandlerLinux or PortHandlerWindows
int port_num = portHandler(DEVICENAME);
portHandler() function sets port path as DEVICENAME and get port_num, and prepares an appropriate functions for port control in controller OS automatically. port_num would be used in many functions in the body of the code to specify the port for use.

// Initialize PacketHandler Structs
packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

// Initialize Groupbulkread Structs
int group_num = groupBulkRead(port_num, PROTOCOL_VERSION);
groupBulkRead() function initializes grouped parameters used for packet construction and packet storing. The utility functions of bulk read deals simultaneously with more than one Dynamixel through #port_num port, building packets by the function which uses PROTOCOL_VERSION.

int index = 0;
int dxl_comm_result = COMM_TX_FAIL; // Communication result
bool dxl_addparam_result = false; // AddParam result
bool dxl_getdata_result = false; // GetParam result
int dxl_goal_position[2] = {DXL_MINIMUM_POSITION_VALUE, DXL_MAXIMUM_POSITION_VALUE}; // Goal position

uint8_t dxl_error = 0; // Dynamixel error
uint16_t dxl1_present_position = 0; // Present position
uint8_t dxl2_moving = 0; // Dynamixel moving status
index variable points the direction to where the Dynamixel should be rotated.
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_addparam_result indicates the result of parameter addition used for sync/bulk related functions
dxl_getdata_result indicates the result of data reception used for sync/bulk related functions
dxl_goal_position stores goal points of Dynamixel rotation.
dxl_error shows the internal error in Dynamixel.
dxl1_present_position views where now Dynamixel DXL1_ID points out.
dxl2_moving views whether the Dynamixel is stopped.

// Open port
if (openPort(port_num))
{
    printf("Succeeded to open the port!\n");
}
else
{
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    _getch();
    return 0;
}
First, controller opens #port_num port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.
// Set port baudrate
if (setBaudRate(port_num, BAUDRATE))
{
    printf("Succeeded to change the baudrate!\n");
}
else
{
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    _getch();
    return 0;
}
Secondly, the controller sets the communication BAUDRATE at #port_num port opened previously.
// Enable Dynamixel#1 Torque
write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
{
  printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
}
else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
{
  printRxPacketError(PROTOCOL_VERSION, dxl_error);
}
else
{
  printf("Dynamixel#%d has been successfully connected \n", DXL1_ID);
}

// Enable Dynamixel#2 Torque
write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_ENABLE);
if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
{
  printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
}
else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
{
  printRxPacketError(PROTOCOL_VERSION, dxl_error);
}
else
{
  printf("Dynamixel#%d has been successfully connected \n", DXL2_ID);
}
As mentioned in the document, above code enables each Dynamixel`s torque to set their status as being ready to move.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num port, writing 1 byte of TORQUE_ENABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error.
getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

// Add parameter storage for Dynamixel#1 present position value
dxl_addparam_result = groupBulkReadAddParam(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
if (dxl_addparam_result != True)
{
  fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL1_ID);
  return 0;
}

// Add parameter storage for Dynamixel#2 present moving value
dxl_addparam_result = groupBulkReadAddParam(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
if (dxl_addparam_result != True)
{
  fprintf(stderr, "[ID:%03d] groupBulkRead addparam failed", DXL2_ID);
  return 0;
}
groupBulkReadAddParam() function stores the Dynamixel ID and address ADDR_MX_MOVING, byte length LEN_MX_MOVING of required data to the bulkread target Dynamixel list.

while (1)
{
  printf("Press any key to continue! (or press ESC to quit!)\n");
  if (getch() == ESC_ASCII_VALUE)
    break;

  // Write Dynamixel#1 goal position
  write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Write Dynamixel#2 goal position
  write2ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_GOAL_POSITION, dxl_goal_position[index]);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  do
  {
    // Bulkread present position and moving status
    groupBulkReadTxRxPacket(group_num);
    if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
      printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);

    dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);
    if (dxl_getdata_result != True)
    {
      fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL1_ID);
      return 0;
    }

    dxl_getdata_result = groupBulkReadIsAvailable(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);
    if (dxl_getdata_result != True)
    {
      fprintf(stderr, "[ID:%03d] groupBulkRead getdata failed", DXL2_ID);
      return 0;
    }

    // Get Dynamixel#1 present position value
    dxl1_present_position = groupBulkReadGetData(group_num, DXL1_ID, ADDR_MX_PRESENT_POSITION, LEN_MX_PRESENT_POSITION);

    // Get Dynamixel#2 moving status value
    dxl2_moving = groupBulkReadGetData(group_num, DXL2_ID, ADDR_MX_MOVING, LEN_MX_MOVING);

    printf("[ID:%03d] Present Position : %d \t [ID:%03d] Is Moving : %d\n", DXL1_ID, dxl1_present_position, DXL2_ID, dxl2_moving);

  } while (abs(dxl_goal_position[index] - dxl1_present_position) > DXL_MOVING_STATUS_THRESHOLD);

  // Change goal position
  if (index == 0)
  {
    index = 1;
  }
  else
  {
    index = 0;
  }
}
During while() loop, the controller writes and reads each Dynamixel position or mov ing status through packet transmission/reception(Tx/Rx).
To continue their rotation, press any key except ESC.
write2ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num port, writing 2 byte of dxl_goal_position[index] value to ADDR_MX_GOAL_POSITION address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
groupBulkReadTxRxPacket() function orders to the Dynamixel #DXL1_ID and #DXL2_ID at the same time through #port_num port, making it possible to require data bytes from different address. (In this example, LEN_MX_PRESENT_POSITION bytes of the values to the address ADDR_MX_PRESENT_POSITION and LEN_MX_MOVING bytes of the values to the address ADDR_MX_MOVING, each.) The function checks Tx/Rx result. getLastTxRxResult() function gets it, and then printTxRxResult() function shows result on the console window if any communication error has been occurred.
groupBulkReadIsAvailable() function checks if available data is in the groupbulkread data storage. The function returns false if no data is available in the storage.
groupBulkReadGetData() function pop the data received by groupBulkReadTxRxPacket() function out. In the example, it stores LEN_MX_PRESENT_POSITION byte data got from ADDR_MX_PRESENT_POSITION address of DXL1_ID Dynamixel and LEN_MX_MOVING byte data got from ADDR_MX_MOVING address of DXL2_ID Dynamixel, each.
groupBulkReadClearParam() function clears the Dynamixel list of groupbulkread.
Reading their present position will be ended when absolute value of (dxl_goal_position[index] - dxl1_present_position) becomes smaller then DXL_MOVING_STATUS_THRESHOLD.
At last, it changes their direction to the counter-wise and waits for extra key input.

// Disable Dynamixel#1 Torque
write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL1_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
{
  printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
}
else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
{
  printRxPacketError(PROTOCOL_VERSION, dxl_error);
}

// Disable Dynamixel#2 Torque
write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL2_ID, ADDR_MX_TORQUE_ENABLE, TORQUE_DISABLE);
if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
{
  printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
}
else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
{
  printRxPacketError(PROTOCOL_VERSION, dxl_error);
}
The controller frees the Dynamixels to be idle.
write1ByteTxRx() function orders to the #DXL1_ID and #DXL2_ID Dynamixels in PROTOCOL_VERSION communication protocol through #port_num port, writing 1 byte of TORQUE_DISABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error.
getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
// Close port
closePort(port_num);

return 0;
Finally, port becomes disposed.
© 2019 ROBOTIS. Powered by Jekyll & Minimal Mistakes.

### C Ping Protocol 1.0
- Description
  This example pings Dynamixel. The ping returns Dynamixel’s Model Number. Ping is commonly used to verify that Dynamixel is successfully connected.
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
/*
* ping.c
*
* Created on: 2016. 5. 16.
* Author: Leon Ryu Woon Jung
*/

//
// ********* ping Example *********
//
//
// Available Dynamixel model on this example : All models using Protocol 1.0
// This example is designed for using a Dynamixel MX-28, and an USB2DYNAMIXEL.
// To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
// Be sure that Dynamixel MX properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000 [1M])
//

#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

#include <stdio.h>
#include "dynamixel_sdk.h" // Uses Dynamixel SDK library

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

// Default setting
#define DXL_ID 1 // Dynamixel ID: 1
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl_model_number; // Dynamixel model number

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Try to ping the Dynamixel
  // Get Dynamixel model number
  dxl_model_number = pingGetModelNum(port_num, PROTOCOL_VERSION, DXL_ID);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  printf("[ID:%03d] ping Succeeded. Dynamixel model number : %d\n", DXL_ID, dxl_model_number);

  // Close port
  closePort(port_num);

  return 0;
}
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif
This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL_ID 1 // Dynamixel ID: 1
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"
Here we set some variables to let you freely change them and use them to run the example code.
As the document previously said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl_model_number; // Dynamixel model number

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Try to ping the Dynamixel
  // Get Dynamixel model number
  dxl_model_number = pingGetModelNum(port_num, PROTOCOL_VERSION, DXL_ID);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  printf("[ID:%03d] ping Succeeded. Dynamixel model number : %d\n", DXL_ID, dxl_model_number);

  // Close port
  closePort(port_num);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);
portHandler() function sets port path as DEVICENAME and get port_num, and prepares an appropriate functions for port control in controller OS automatically. port_num would be used in many functions in the body of the code to specify the port for use.

  // Initialize PacketHandler Structs
  packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint16_t dxl_model_number; // Dynamixel model number
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_error shows the internal error in Dynamixel.
dxl_model_number keeps Dynamixel model number.

  // Open port
  if (openPort(port_num))
  {
      printf("Succeeded to open the port!\n");
  }
  else
  {
      printf("Failed to open the port!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
First, controller opens #port_num port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
      printf("Succeeded to change the baudrate!\n");
  }
  else
  {
      printf("Failed to change the baudrate!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Secondly, the controller sets the communication BAUDRATE at #port_num port opened previously.

  dxl_model_number = pingGetModelNum(port_num, PROTOCOL_VERSION, DXL_ID);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
pingGetModelNum() function orders to the #DXL_ID Dynamixel through #port_num port. Then, it receives the dxl_model_number. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.
  // Close port
  closePort(port_num);

  return 0;
Finally, port becomes disposed.
© 2019 ROBOTIS. Powered by Jekyll & Minimal Mistakes.

### C Reset Protocol 1.0
- Description
  This example resets all Dynamixel settings to factory defaults, including rate ID (1) and baud rate (57600 bps):
- Supported Dynamixels
  Protocol 1.0 Dynamixels
#### Sample code
/*
* reset.c
*
* Created on: 2016. 5. 16.
* Author: Leon Ryu Woon Jung
*/

//
// ********* Factory Reset Example *********
//
//
// Available Dynamixel model on this example : All models using Protocol 1.0
// This example is designed for using a Dynamixel MX-28, and an USB2DYNAMIXEL.
// To use another Dynamixel model, such as X series, see their details in E-Manual(support.robotis.com) and edit below "#define"d variables yourself.
// Be sure that Dynamixel PRO properties are already set as %% ID : 1 / Baudnum : 1 (Baudrate : 1000000 [1M])
//

// Be aware that:
// This example resets all properties of Dynamixel to default values, such as %% ID : 1 / Baudnum : 34 (Baudrate : 57600)
//

#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif

#include <stdio.h>
#include "dynamixel_sdk.h" // Uses Dynamixel SDK library

// Control table address
#define ADDR_MX_BAUDRATE 4 // Control table address is different in Dynamixel model

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel

// Default setting
#define DXL_ID 1 // Dynamixel ID: 1
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define FACTORYRST_DEFAULTBAUDRATE 57600 // Dynamixel baudrate set by factoryreset
#define NEW_BAUDNUM 1 // New baudnum to recover Dynamixel baudrate as it was
#define OPERATION_MODE 0x00 // Mode is unavailable in Protocol 1.0 Reset

#define TORQUE_ENABLE 1 // Value for enabling the torque
#define TORQUE_DISABLE 0 // Value for disabling the torque

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}

void msecSleep(int waitTime)
{
#ifdef __linux__
    usleep(waitTime * 1000);
#elif defined(_WIN32) || defined(_WIN64)
    Sleep(waitTime);
#endif
}

int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint8_t dxl_baudnum_read; // Read baudnum

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Read present baudrate of the controller
  printf("Now the controller baudrate is : %d\n", getBaudRate(port_num));

  // Try factoryreset
  printf("[ID:%03d] Try factoryreset : ", DXL_ID);
  factoryReset(port_num, PROTOCOL_VERSION, DXL_ID, OPERATION_MODE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printf("Aborted\n");
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    return 0;
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Wait for reset
  printf("Wait for reset...\n");
  msecSleep(2000);

  printf("[ID:%03d] factoryReset Success!\n", DXL_ID);

  // Set controller baudrate to dxl default baudrate
  if (setBaudRate(port_num, FACTORYRST_DEFAULTBAUDRATE))
  {
    printf("Succeed to change the controller baudrate to : %d\n", FACTORYRST_DEFAULTBAUDRATE);
  }
  else
  {
    printf("Failed to change the controller baudrate\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }

  // Write new baudnum
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE, NEW_BAUDNUM);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Set Dynamixel baudnum to : %d\n", DXL_ID, NEW_BAUDNUM);
  }

  // Set port baudrate to BAUDRATE
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeed to change the controller baudrate to : %d\n", BAUDRATE);
  }
  else
  {
    printf("Failed to change the controller baudrate\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  msecSleep(200);

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel Baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }

  // Close port
  closePort(port_num);

  return 0;
}
#### Details
#ifdef __linux__
#include <unistd.h>
#include <fcntl.h>
#include <termios.h>
#elif defined(_WIN32) || defined(_WIN64)
#include <conio.h>
#endif
This source includes above to get key input interruption while the example is running. Actual functions for getting the input is described in a little below.

#include <stdio.h>
The example shows Dynamixel status in sequence by the function printf(). So here stdio.h is needed.

#include "dynamixel_sdk.h" // Uses Dynamixel SDK library
All libraries of Dynamixel SDK are linked with the header file dynamixel_sdk.h.

// Control table address
#define ADDR_MX_BAUDRATE 4 // Control table address is different in Dynamixel model
Dynamixel series have their own control tables: Addresses and Byte Length in each items. To control one of the items, its address (and length if necessary) is required. Find your requirements in http://emanual.robotis.com/.

// Protocol version
#define PROTOCOL_VERSION 1.0 // See which protocol version is used in the Dynamixel
Dynamixel uses either or both protocols: Protocol 1.0 and Protocol 2.0. Choose one of the Protocol which is appropriate in the Dynamixel.

// Default setting
#define DXL_ID 1 // Dynamixel ID: 1
#define BAUDRATE 1000000
#define DEVICENAME "/dev/ttyUSB0" // Check which port is being used on your controller
        // ex) Windows: "COM1" Linux: "/dev/ttyUSB0"

#define FACTORYRST_DEFAULTBAUDRATE 57600 // Dynamixel baudrate set by factoryreset
#define NEW_BAUDNUM 1 // New baudnum to recover Dynamixel baudrate as it was
#define OPERATION_MODE 0x00 // Mode is unavailable in Protocol 1.0 Reset
Here we set some variables to let you freely change them and use them to run the example code.
As the document previously said in previous chapter, customize Dynamixel control table items, such as DXL_ID number, communication BAUDRATE, and the DEVICENAME, on your own terms of needs. In particular, BAUDRATE and DEVICENAME have systematical dependencies on your controller, so make clear what kind of communication method you will use.
Since the factory reset recovers the Dynamixel control table items to the original state, the baudrate of controller serial port should be set to its changed baudrate(FACTORYRST_DEFAULTBAUDRATE : 57600 bps) as well. After that, controller sets its baudrate to the value (1000000 bps : NEW_BAUDNUM = 1) before factory reset.
In Protocol 1.0, only one mode that resets whole items is avaiable.

int getch()
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  ch = getchar();
  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  return ch;
#elif defined(_WIN32) || defined(_WIN64)
  return _getch();
#endif
}

int kbhit(void)
{
#ifdef __linux__
  struct termios oldt, newt;
  int ch;
  int oldf;

  tcgetattr(STDIN_FILENO, &oldt);
  newt = oldt;
  newt.c_lflag &= ~(ICANON | ECHO);
  tcsetattr(STDIN_FILENO, TCSANOW, &newt);
  oldf = fcntl(STDIN_FILENO, F_GETFL, 0);
  fcntl(STDIN_FILENO, F_SETFL, oldf | O_NONBLOCK);

  ch = getchar();

  tcsetattr(STDIN_FILENO, TCSANOW, &oldt);
  fcntl(STDIN_FILENO, F_SETFL, oldf);

  if (ch != EOF)
  {
    ungetc(ch, stdin);
    return 1;
  }

  return 0;
#elif defined(_WIN32) || defined(_WIN64)
  return _kbhit();
#endif
}
These functions accept the key inputs in terms of example action. The example codes mainly apply the function getch() rather than the function kbhit() to get information which key has been pressed.
void msecSleep(int waitTime)
{
#ifdef __linux__
    usleep(waitTime * 1000);
#elif defined(_WIN32) || defined(_WIN64)
    Sleep(waitTime);
#endif
}
msecSleep() function halt the computational process in which this function is used.
int main()
{
  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);

  // Initialize PacketHandler Structs
  packetHandler();

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint8_t dxl_baudnum_read; // Read baudnum

  // Open port
  if (openPort(port_num))
  {
    printf("Succeeded to open the port!\n");
  }
  else
  {
    printf("Failed to open the port!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeeded to change the baudrate!\n");
  }
  else
  {
    printf("Failed to change the baudrate!\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Read present baudrate of the controller
  printf("Now the controller baudrate is : %d\n", getBaudRate(port_num));

  // Try factoryreset
  printf("[ID:%03d] Try factoryreset : ", DXL_ID);
  factoryReset(port_num, PROTOCOL_VERSION, DXL_ID, OPERATION_MODE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printf("Aborted\n");
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
    return 0;
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }

  // Wait for reset
  printf("Wait for reset...\n");
  msecSleep(2000);

  printf("[ID:%03d] factoryReset Success!\n", DXL_ID);

  // Set controller baudrate to dxl default baudrate
  if (setBaudRate(port_num, FACTORYRST_DEFAULTBAUDRATE))
  {
    printf("Succeed to change the controller baudrate to : %d\n", FACTORYRST_DEFAULTBAUDRATE);
  }
  else
  {
    printf("Failed to change the controller baudrate\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }

  // Write new baudnum
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE, NEW_BAUDNUM);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Set Dynamixel baudnum to : %d\n", DXL_ID, NEW_BAUDNUM);
  }

  // Set port baudrate to BAUDRATE
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeed to change the controller baudrate to : %d\n", BAUDRATE);
  }
  else
  {
    printf("Failed to change the controller baudrate\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  msecSleep(200);

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel Baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }

  // Close port
  closePort(port_num);

  return 0;
}
In main() function, the codes call actual functions for Dynamixel control.

  // Initialize PortHandler Structs
  // Set the port path
  // Get methods and members of PortHandlerLinux or PortHandlerWindows
  int port_num = portHandler(DEVICENAME);
portHandler() function sets port path as DEVICENAME and get port_num, and prepares an appropriate functions for port control in controller OS automatically. port_num would be used in many functions in the body of the code to specify the port for use.

  // Initialize PacketHandler Structs
  packetHandler();
packetHandler() function initializes parameters used for packet construction and packet storing.

  int dxl_comm_result = COMM_TX_FAIL; // Communication result

  uint8_t dxl_error = 0; // Dynamixel error
  uint8_t dxl_baudnum_read; // Read baudnum
dxl_comm_result indicates which error has been occurred during packet communication.
dxl_error shows the internal error in Dynamixel.
dxl_baudnum_read keeps Dynamixel baudrate.

  // Open port
  if (openPort(port_num))
  {
      printf("Succeeded to open the port!\n");
  }
  else
  {
      printf("Failed to open the port!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
First, controller opens #port_num port to do serial communication with the Dynamixel. If it fails to open the port, the example will be terminated.

  // Set port baudrate
  if (setBaudRate(port_num, BAUDRATE))
  {
      printf("Succeeded to change the baudrate!\n");
  }
  else
  {
      printf("Failed to change the baudrate!\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Secondly, the controller sets the communication BAUDRATE at #port_num port opened previously.

  // Read present baudrate of the controller
  printf("Now the controller baudrate is : %d\n", getBaudRate(port_num));
getBaudRate() function shows which baudrate is used in #port_num port of the controller.
  factoryReset(port_num, PROTOCOL_VERSION, DXL_ID, OPERATION_MODE);
factoryReset() function orders to the #DXL_ID Dynamixel through #port_num port, executing it to be reset as OPERATION_MODE format. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

  // Wait for reset
  printf("Wait for reset...\n");
  msecSleep(2000);
Factory reset takes few seconds.

  // Set controller baudrate to dxl default baudrate
  if (setBaudRate(port_num, FACTORYRST_DEFAULTBAUDRATE))
  {
      printf("Succeed to change the controller baudrate to : %d\n", FACTORYRST_DEFAULTBAUDRATE);
  }
  else
  {
      printf("Failed to change the controller baudrate\n");
      printf("Press any key to terminate...\n");
      _getch();
      return 0;
  }
Controller should change its baudrate itself to do the communication with initialized Dynamixel.

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }
This shows that reconnection between controller and Dynamixel is happened by adjusting the baudrate.
  // Write new baudnum
  write1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE, NEW_BAUDNUM);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Set Dynamixel baudnum to : %d\n", DXL_ID, NEW_BAUDNUM);
  }
To make the Dynamixel into previous condition, write1ByteTxRx() function orders to the #DXL_ID Dynamixel in PROTOCOL_VERSION communication protocol through #port_num port, writing 1 byte of TORQUE_ENABLE value to ADDR_MX_TORQUE_ENABLE address. The function checks Tx/Rx result and receives Hardware error. getLastTxRxResult() function and getLastRxPacketError() function get either, and then printTxRxResult() function and printRxPacketError() function show results on the console window if any communication error or Hardware error has been occurred.

  // Set port baudrate to BAUDRATE
  if (setBaudRate(port_num, BAUDRATE))
  {
    printf("Succeed to change the controller baudrate to : %d\n", BAUDRATE);
  }
  else
  {
    printf("Failed to change the controller baudrate\n");
    printf("Press any key to terminate...\n");
    getch();
    return 0;
  }

  msecSleep(200);

  // Read Dynamixel baudnum
  dxl_baudnum_read = read1ByteTxRx(port_num, PROTOCOL_VERSION, DXL_ID, ADDR_MX_BAUDRATE);
  if ((dxl_comm_result = getLastTxRxResult(port_num, PROTOCOL_VERSION)) != COMM_SUCCESS)
  {
    printTxRxResult(PROTOCOL_VERSION, dxl_comm_result);
  }
  else if ((dxl_error = getLastRxPacketError(port_num, PROTOCOL_VERSION)) != 0)
  {
    printRxPacketError(PROTOCOL_VERSION, dxl_error);
  }
  else
  {
    printf("[ID:%03d] Dynamixel Baudnum is now : %d\n", DXL_ID, dxl_baudnum_read);
  }

These changes controller baudrate and verify that the Dynamixel has been successfully set into previous state.
  // Close port
  closePort(port_num);

  return 0;
Finally, port becomes disposed.
© 2019 ROBOTIS. Powered by Jekyll & Minimal Mistakes.